| # Betaflight / STM32F411 (S411) 4.0.0 |
| --- |
|  | board_name IFF411PRO |
|  | manufacturer_id IFRC |
|  | # resources |
|  | resource BEEPER 1 B02 |
|  | resource MOTOR 1 A00 |
|  | resource MOTOR 2 B10 |
|  | resource MOTOR 3 B06 |
|  | resource MOTOR 4 B07 |
|  | resource PPM 1 A03 |
|  | resource LED_STRIP 1 A08 |
|  | resource SERIAL_TX 1 A09 |
|  | resource SERIAL_TX 2 A02 |
|  | resource SERIAL_RX 1 A10 |
|  | resource SERIAL_RX 2 A03 |
|  | resource I2C_SCL 1 B08 |
|  | resource I2C_SDA 1 B09 |
|  | resource LED 1 C13 |
|  | resource LED 2 C14 |
|  | resource SPI_SCK 1 A05 |
|  | resource SPI_SCK 2 B13 |
|  | resource SPI_SCK 3 B03 |
|  | resource SPI_MISO 1 A06 |
|  | resource SPI_MISO 2 B14 |
|  | resource SPI_MISO 3 B04 |
|  | resource SPI_MOSI 1 A07 |
|  | resource SPI_MOSI 2 B15 |
|  | resource SPI_MOSI 3 B05 |
|  | resource ADC_BATT 1 B00 |
|  | resource ADC_CURR 1 B01 |
|  | resource FLASH_CS 1 A15 |
|  | resource OSD_CS 1 B12 |
|  | resource GYRO_EXTI 1 A01 |
|  | resource GYRO_CS 1 A04 |
|  | resource USB_DETECT 1 C15 |
|  | # timer |
|  | timer A03 AF3 |
|  | # pin A03: TIM9 CH2 (AF3) |
|  | timer A00 AF1 |
|  | # pin A00: TIM2 CH1 (AF1) |
|  | timer B10 AF1 |
|  | # pin B10: TIM2 CH3 (AF1) |
|  | timer B06 AF2 |
|  | # pin B06: TIM4 CH1 (AF2) |
|  | timer B07 AF2 |
|  | # pin B07: TIM4 CH2 (AF2) |
|  | timer A08 AF1 |
|  | # pin A08: TIM1 CH1 (AF1) |
|  | # dma |
|  | dma ADC 1 0 |
|  | # ADC 1: DMA2 Stream 0 Channel 0 |
|  | dma pin A00 0 |
|  | # pin A00: DMA1 Stream 5 Channel 3 |
|  | dma pin B10 0 |
|  | # pin B10: DMA1 Stream 1 Channel 3 |
|  | dma pin B06 0 |
|  | # pin B06: DMA1 Stream 0 Channel 2 |
|  | dma pin B07 0 |
|  | # pin B07: DMA1 Stream 3 Channel 2 |
|  | dma pin A08 0 |
|  | # pin A08: DMA2 Stream 6 Channel 0 |
|  | # master |
|  | set baro_bustype = I2C |
|  | set baro_i2c_device = 1 |
|  | set blackbox_device = SPIFLASH |
|  | set current_meter = ADC |
|  | set battery_meter = ADC |
|  | set system_hse_mhz = 8 |
|  | set max7456_spi_bus = 2 |
|  | set flash_spi_bus = 3 |
|  | set gyro_1_bustype = SPI |
|  | set gyro_1_spibus = 1 |
|  | set gyro_1_sensor_align = CW0 |
|  | set beeper_inversion = ON |
|  | set beeper_od = OFF |