Infrared Thermal Imager

Specification

Millerfair, make technology with temperature.

# Product

# Screen

Automatic tracking hot & cold spots, Infrared & visible fusion

# Features

- TFT full view color screen display

- Dual MCU processors, refresh faster

- Low power consumption, super endurance

- Hot and cold point temperature markers can guide users to the areas with the highest and lowest temperature in the thermal image.

- Selectable pallette

- Hybrid imaging of visual and infrared images

- Images capture saved in SD card

- Hybrid imaging of visual and infrared images stored in instrument directly.

- Connect USB with other power supply and meter, Use a power supply to meter directly.

# Technical Data

| Infrared Image Resolution | 32*32 (1024 pixels) |
| --- | --- |
| Display Resolution | 240*320 pixels |
| Visual Image Resolution | 300000 pixels |
| Field Angle | 33*33 degrees |
| Infrared Temp. Range | ‘-20~380℃ 、 -4~716℉ |
| Accuracy | >0℃，± 2% or reading ± 2℃ / 3.6℉ |
|  | <0℃，± 3℃ / 5.4℉ |
|  | Note: Accuracy is measured in an |
|  | environment of 18-28 degrees |
| Ambient Temp. Range | ’-20~70℃ / -4~158℉ |
| Accuracy | 1.0 ℃ / 1.8℉ |
| Ambient Humidity Range | 0~100% RH |
| Accuracy | 35~70% RH:+3.0% RH |
|  | Others +4.0% RH |
| Dew Point Temp. Range | ’-30~100℃ / -22~212℉ |
| Accuracy | ±1.0℃/ 1.8℉ (25℃ / 77℉,35~70% RH) |
| Wet Bulb Temp. Rang | ’-30~100℃ / -22~212℉ |
| Accuracy | ±1.0℃/ 1.8℉ (25℃ / 77℉,35~70% RH) |
| Mininum Focal Length | 0.5m |
| Thermal Sensitivity | 0.15℃/ 0.27℉ |
| Emissivity | Adjustable 0.1~1.0 |
| Image Capture Frequency | 9HZ |
| Wavelength | 8~14um |
| Focus Mode | Fixed |
| Palette | Ink color,black and white, rainbow color, |
|  | ocean blue, iron red |
| View Options | Blending of the visual and the infrared from |
|  | full infrared to full visual in 25% steps |
| File Format | BMP |
| Storage | 8GB Micro SD Card |
| Memory View | Scroll all saved images and view them on the screen |
| USB function | Connect USB cable with PC, meter works as U disk,stored data in SD card can be downlowd to computer directly, connected USB cable with other power supply to the meter directly and meter works as usual during this time |
| Auto Power Off | 3 minutes, 5 minutes, 10 minutes are optional |
| Working Temperature | ‘ -5~40℃ / 23~104 ℉ |
| Storage Temp. Range | ‘ -20~55℃ / -4~131 ℉ |
| Relative Humidity | 10~80% RH |
| Over-range Indication | OVER |
| Power Supply | 4*LR6 AA battery and USB power supply |

# Off/On Operation

- Put on battery, hold down EXIT button until screen into start interface.

- To off machine, please hold down EXIT button about 3 seconds until the screen into count down interface.

# Main menu description

Click OK enter main menu, and select the corresponding icon through the up or down key to set.

# Secondary Menu description

## Storage image

Select “storage image” and press OK, enter into menu setting mode. Select OK key enter to image list and view the saved image, click OK key to see the specific image, press the UP key or DOWN key to switch and image, then press the OK key again to delete the image. Press EXIT key to exit the specific image view and return to the image list, continue to press EXIT key to return to the main menu.

## Pallet setting

Select “Pallet setting image” and press OK key, the five modes of pallette can be switched in turn: ink color, black and white, rainbow color, ocean blue and iron red.

## Emissivity setting

Select “ emissivity setting image” and press OK key to do emissivity setting. By press UP key and down key , we can select the preset emissivity of 0.95、0.8、0.6、0.3 and custom emissivity, then press EXIT key to finish setting and return.

## Temperature setting

Select “temperature setting image”, press OK key to switch temperature unit of ℃ and ℉ .

## Temperature mark switch

Select “Temperature mark switch image”, press OK key to switch temperature mark on-off, ON: open temperature mark, OFF: close temperature mark.

## Memory card capacity

It shows the residual capacity. To export the pictures in SD card, when the thermal imager is turned on, the mobile disk will pop up automatically after directly connecting to the computer through the micro USB data cable. We can view the pictures in SD card, copy and delete the pictures.

## Time setting

Select “Time setting image”, press OK key to enter time setting mode, press UP and DOWN key to choose the desired value. Press OK key to switch the setting of year, month, day, hour and minute in turn. Press EXIT key to save the time settings and return to main menu.

## Backlight setting

Select “Backlight setting image”, press OK key,the brightness of the screen is set by pressing UP and DOWN key, the bigger the value, the brighter the screen. Select the appropriate brightness, press the EXIT key to finish setting and return.

## Timed auto_shutdown

OFF: None timed shutdown

Without operating the instrument

3 MIN: turn off after 3 minutes

5 MIN: turn off after 5 minutes

10 MIN: turn off after 10 minutes

# Attention

All objects radiate infrared energy, which is based on the actual surface temperature and surface radiation coefficient of the object. The product perceives the infrared energy on the surface of the object and uses the data to calculate the estimated temperature, many common objects and materials ( suc as painted metal wood, water, skin and fabric) can radiate energy effectively, so it is easy to obtain relatively accurate measurements, for the surface which is easy to radiate energy ( high radiation coefficient), the radiation does not apply to flossy surfaces or painted metals because their radiation coefficients are less than 60% (0.6), these materials are not easy to radiate energy and are classified as low radiation coefficient materials. In order to measure the materials with lower radiation coefficient more accurately, it is necessary to correct the radiation coefficient, adjusting the radiation value usually enables the product to calculate the actual temperature more accurately.