MR300 SWR Analyzer

User Manual

Revision 161208

This product is revised by SARK100, and the technology is from Melchor Varel(EA4FRB)

December 8, 2016

- 0-

MR300 SWR Analyzer

1   Specifications

Frequency Generation & Control:

o

o

o

o

o

1 - 60 Mhz

Source impedance: 50 Ohms

Stability: +/- 100 ppm

Spectral Purity: Harmonics down >- TBD dB beyond 60 MHz

Step Size: User configurable increments of 100 Hz, 1 kHz, 10 kHz, and 100 kHz

Usable Measurement Range:

o   SWR: 1.0 to 9.99

o

Impedance: approx. 5 to 2000 ohms

RF Output:

o

Adjustable: 2.0 Volts pp (typ)

Power supply:

o

External: 13.8 to 19 Volts DC, 500mA (Note:12V can be used but can not be

used for recharged)

o

o

Internal: 8xAAA 1000mAh NiMH cells

Charging time: 12 hours (charge rate 0.1C)

Controls:

o

o

Pushbuttons (5): "Mode", "Band", "Config", "Scan", "Up", "Down"

Switch: "Power On"

Connectors:

o

o

o

RF Out: M (SL16)

USB: Mini-B receptacle

External power: 2.1mm Power Jack (center pin positive)

InstrumentCapabilities:

o

Measure   antenna  electrical   parameters:   SWR,   impedance  (resistance   +

reactance), capacitance, inductance

o

Measure feedpoint impedance

December 8, 2016

- 1-

MR300 SWR Analyzer

o

Measure ground loss

o

o

o

Adjust antenna tuners and determine loss

Measure inductors and capacitors

Measure coax  transmission line (SWR,  length, velocity  factor, approximate  Q

and loss, resonant frequency, and impedance)

o

Measure and determine optimum  settings for tuning stubs:  SWR, approximate

Q, resonant frequency, bandwidth, impedance

o

o

o

o

o

o

o

Determine characteristic impedance of transmission line

Determine length of ¼ and ½ wave phasing lines

Coaxial Cable Loss

Determine antenna tuner loss

Measure balun loss

Measure inductor Q

Estimate quartz crystal parameters

December 8, 2016

- 2-

MR300 SWR Analyzer

2   Connections and Controls

December 8, 2016

- 3-

MR300 SWR Analyzer

3   Connections and Controls

Power-on

Power  is  turned on  to  the  MR300  by  sliding the  switch  located  on  the  bottom  panel. After

power-on the unit will display for half a second the following welcome message:

HR Antenna Analyzer

www.lxqqfy.com

Then the instrument  automatically switches to  impedance  mode  that  is the  default mode  and

LCD shows  frequency,  SWR, and  the  magnitude of  the  impedance:

SWR   14,100.000

>10

Z=2000

The analyzer  has an  automatic power-save  function. This  function detects  that no  button was

pressed after a user programmable  time and goes into a power saving  state and which turns off

the display.  In this  state the press  of any  button will start  immediately the unit  returning to  the

same state before  the suspension, i.e. the  same function and frequency  selected. This function

can be disabled by the user.

It  is important  to  note  that this  is  an  energy saving  feature  but  not a  full  power-off, i.e.  the

instrument  continues to  have  a significant  consumption  so it  is  recommended  shutting down

completely in the case it s not going to be used.

User Interface

The user interface consists of six buttons, four aimed at selecting the functions available and two

are used  primarily to select  the frequency but  have the  dual function of  canceling and validate

respectively. All functions are summarized in the Appendix E:

Adjusting the Frequency

Frequency is changed  by adjusting a  single digit indicated at  the point in  the display where the

cursor ‘_’  is by pressing either  frequency change button.  Upon power-up of  the instrument, the

10 kHz digit is the adjustment point, as shown by the digit with the cursor in the display below.

SWR 14,100.000

1.02 Z = 40Ω

To  move  the  cursor  to a  different  digit  to  be  adjusted,  press  simultaneously  the frequency

change buttons. The  cursor will move  to any of  the seven available digits,  allowing subsequent

up/down adjustment  of that digit  after pressing  again the frequency  change buttons. A  blinking

cursor will be display during the digit adjustment mode.

December 8, 2016

- 4-

MR300 SWR Analyzer

SWR 14,10.000

1.02 Z = 40Ω

Pressing the  left button will  increase the digit  value and, correspondingly,  the signal  generated

by the unit. Pressing the right button will decrease the digit and the generated signal.

When  the digit  is incremented  past 9,  or when  it is  decremented past  0, the  digits above  the

selected adjustment  point are rolled  up or down,  respectively. Using this  frequency adjustment

scheme, the user can conveniently pick  an “increment” digit and manually scan frequencies with

the desired granularity.  Rough scans can manually be  done by positioning the  cursor under the

100 kHz digit  or the 1 MHz  digit, giving a wide and  course scan of the  frequencies with a quick

twist of the dial.

The  signal frequency  can  then  be set  to  the  area of  interest  and  the cursor  set  to  a lower

granular digit (e.g., 10 kHz or 1 kHz) in order to manually perform a detailed scan  while watching

displayed results for SWR, impedance and reactance.

MODE

Successively pressing  the  MODE button  you can  select one  of  the MR300  operating modes:

impedance (magnitude), complex impedance, capacitance, inductance, and off.

Impedance Mode (magnitude)

This is  the  main mode  of the  instrument and  measures the  SWR  and the magnitude  of the

impedance. An example screen is the following:

SWR   14,100.000

1.02

Z = 40Ω

•

•

•

The top line indicates the mode and the frequency

The first number on the second line is the SWR, in this case 1.02:1

The second number is the impedance magnitude (modulus), in this case 40  Ω

In  this mode  the  instrument can  be  used  as a  VFO  as it  keeps  the  signal in  the  selected

frequencycontinuously.

Complex Impedance Mode

In this  mode it is measured  the SWR and  the complex impedance.  An example screen is  the

following:

IMP  14,100.000

1.02  45 + j 50

•

•

The top line indicates the mode and the frequency

The first number on the second line is the SWR, in this case 1.02:1

December 8, 2016

- 5-

MR300 SWR Analyzer

•

•

The middle value is the resistance, i.e. the real part of the impedance, in this case 45  Ω

Then it  is shown  the reactance  sign, ‘+’  for inductive  reactance and  ‘-‘ for  capacitive

reactance. If it is not shown, i.e. ‘ ‘ it means that it cannot be determined

•

Last term is the reactance, in this case it is 50 Ω inductive reactance

This mode can not be used as a VFO because the frequency is continuously dizzling in order to

determine the reactance sign.

Capacitance Mode

This mode allows the measurement of the capacitance. An example screen is the following:

CAP   14,100.000

C = 112.4 pF

•

•

The top line indicates the mode and the frequency

The bottom line indicates the capacitance in pF

Capacity  values  must  be  within  the  measurement  range  of  the  instrument.  Given  that  the

maximum impedance  specification for  the analyzer is  2000 Ω,  the display will  show a numeric

value only when the reactance is less than this value. The formula to calculate the capacity is the

following:

1

XC  =

2×  pi × F ×C

Inductance Mode

This mode allows the measurement of the inductance. An example screen is the following:

IND   14,100.000

L = 7.8 uH

•

•

The top line indicates the mode and the frequency

The bottom line indicates the inductance in uH

Inductance  values must  be  within  the measurement  range  of  the instrument.  Given  that  the

maximum impedance  specification for  the analyzer is  2000 Ω,  the display will  show a numeric

value only when the reactance is  less than this value. The formula to calculate  the inductance is

the following:

XL = 2×  pi× F ×  L

Off Mode

In this mode it is  disabled the DDS and the impedance measurements.It is provided a  RF level

measurement  mode where  the measured  signal level  is  displayed in  the second  line  of the

December 8, 2016

- 6-

MR300 SWR Analyzer

display as  a bar  graph. This  will be useful  to know  if the  antenna is receiving  a near  RF field

which can interfere with the measurements.

OFF

BAND

The  BAND  button  allows  selecting  the  working  frequency  band  within the  bands  available.

Pressing this button sequentially  selects the next higher band  which value is shown in the  LCD,

and it is changed the frequency. If it is the first time accessing the band, the frequency will be set

to the  middle value.  Otherwise it  will be  set the  previous frequency value,  since this  is stored

when changing the band.

Band

Lower

Middle

Upper

Frequency

Frequency

Frequency

160M

80M

40M

30M

25M

20M

17M

15M

12M

11M

10M

8M

1,000.000

2,000.000

5,000.000

8,000.000

11,000.000

13,000.000

17,000.000

19,000.000

23,000.000

26,000.000

28,000.000

31,000.000

49,000.000

1,800.000

3,700.000

2,000.000

5,000.000

7,100.000

8,000.000

10,100.000

12,000.000

14,100.000

18,100.000

21,000.000

24,900.000

27,000.000

29,000.000

40,000.000

51,000.000

11,000.000

13,000.000

17,000.000

19,000.000

23,000.000

26,000.000

28,000.000

31,000.000

49,000.000

53,000.000

6M

SCAN

Pressing the SCAN pushbutton will automatically sweep the antenna analyzer test signal across

the band  range previously selected,  incrementing from  the lower  frequency limit to  the upper

December 8, 2016

- 7-

MR300 SWR Analyzer

frequency limit,  in  steps according  the programmed  step  value. During  the scan  the  SWR is

measured and updated  on the screen as well  as the current frequency  value. Each SWR value

is compared to  previous value in order to  determine if a minima, or  a “dip”, has occurred at  this

point in  the  scan. If  so,  that data  point is  stored  for later  display. Besides  the 2:1  points  are

stored in order  to determine the bandwidth. An  example screen during the  scan is the following

(frequency and SWR are updated continuously):

SCAN   14,100.200

1.30

Notice that  when detected  the 2:1  SWR  points the buzzer  is sounded  to alert  the user  of the

event. After the scan  process the instrument will show the bandwidth and after  pressing any key

the  instrument will  switch  to impedance  mode  with the  frequency  set to  the  frequency value

corresponding to the minimum SWR point.

BW

35.000

Press any key

In the case  of not finding a  resonance point the unit  will display the following error  message on

the screen.

Err No Matching

Press any key

CONFIG

Successively  pressing  the  CONFIG  button  you  can  select  one  of  the MR300  configuration

modes and extended funtions.  To select either option you  need to press the button VAL  and for

exit you need pressing the button CAN.

PC Link

The  PC Link  function  lets  you control  the  MR300  from  your PC  using  the USB  connection.

The  PC   USB  driver    provides an   emulation  of  a  COM   port  and  the  MR300   provides  a

command  interface  so you  can  be  control  the instrument  from  a  terminal  program  such as

HyperTerminal or any other program designed for this purpose, e.g. PCC-SARK100.

To use  this feature  you must have  installed the  USB driver, see  Appendix A:  and connect the

USB cable.  The COM port setting  is 57600, 8,  n, 1, with  no hardware flow  control. By entering

this function the analyzer will send the following text to the terminal and will display the command

prompt:

SARK SWR Analyzer V05

>>

December 8, 2016

- 8-

MR300 SWR Analyzer

The  available   commands  are   described   in  Appendix   C:  These   can  be   typed  from   the

HyperTerminal window  and  the results  will be  returned to  the terminal.  The  MR300 will  show

the last processed command in the bottom line of the LCD.

Step Size

This function  allows  you to  change the value  of  the frequency step  for the  SCAN and  for the

increase/decrease  frequency  buttons  for  the  impedance  measurement  modes.  Successively

pressing the  CONFIG button you  can select one  of the step  values. To select  either value you

need to press the button VAL and for exit you need pressing the button CAN.

The following values are available: 10Hz, 100Hz, 1kHz, 10kHz, and 100kHz.

Suspend Timeout

This  feature allows  you  to  program the  user  idle time  for  the automatic  power-save  feature.

Successively pressing the CONFIG  button you can select  one of the idle  time values. To select

either value you need to press the button VAL and for exit you need pressing the button CAN.

The following values are available: Off (disabled), 30 seconds, 60 seconds, and 90 seconds.

Calibrate

This function  allows calibrating  the instrument  in order to  get better  accuracy. By  entering this

function the  user  is instructed  to follow  a  series of  steps which  are described  in  detail in  the

Appendix B:

Software Load

Don’t update software.

December 8, 2016

- 9-

MR300 SWR Analyzer

4   Uses for an Antenna Analyzer

The   MR300   antenna   analyzer  is   a   useful   tool   for   the   amateur   radio   station  or   the

homebrewer’s  workbench. This  section  will describe  the basic  uses,  as well  some  advanced

techniques for  which  you can  use the  analyzer to  get intermediate  measurements in  order to

compute the desired result.

4.1 Antenna Measurements

The antenna is simply connected to the analyzer RF output and the analyzer is set to the desired

frequency.  The  instrument  measures the  SWR,  impedance,  resistance,  and  reactance.  The

SCAN function will be helpful to automatically find the resonance frequency and the bandwidth of

the antenna.

4.2 Measure Feed Point Impedance

Connecting the analyzer  directly at the  antenna terminals or remotely  through a halfwavelength

of transmission line allows direct measurement  of the antenna terminal impedance. This is often

useful with vertical antennas.

A matching  network can be  connected to the  antenna and then  adjusted for best  SWR on  the

analyzer.

4.3 Measure Ground Losses

With   short  vertical   antennas,  measuring   the  impedance   directly  at   the  feedpoint   allows

estimation  of  ground  loss  or  loading  coil loss.  For  example  a  ¼  wave  vertical  will  have  a

resistance of about 36 ohms at resonance. Any higher reading indicates ground loss.

Similarly shorter antennas  (when resonated) will  have lower resistance values.  Reading a good

SWR  may mean  excess  loss  and measuring  the  actual impedance  allows  gauging just  how

much loss.

4.4 Adjust Antenna Tuners

The analyzer  can be  used to  adjust an antenna  tuner for  a perfect  match without the  need to

transmit a strong signal from the station rig. The analyzer uses only milliwatts of  power lessening

the possibility of causing interference, see Figure 3.

4.5 CapacitorMeasurement

There are  several  ways to  measure capacitance  with the  MR300. The  simplest  is to  connect

the capacitor across the RF output connector and select  Capacitance from the Mode pushbutton

menu.  You  can  accurately   measure  capacitance  values  as   long  as  the  reactance  at  the

measurement  frequency is  within  the impedance  measurement  specifications of  the  analyzer

(about 10 to 2000 Ω).

December 8, 2016

- 10-

MR300 SWR Analyzer

Another  way to  measure  capacitance  with the  MR300  is to  measure  it  in a  series  resonant

circuit.  (See Figure  1  and Figure  5).  You  will need  an  inductor of  known  value and  a  51  Ω

carbon composition or film  resistor. It is recommended  that a small 5% tolerance  choke with an

inductance of between 1 and 10  uH be used. Common RF chokes are fine  and can be obtained

from most full-service mail order component suppliers.

Figure 1

To measure capacitance by the  second method, connect the components as shown in Figure  1.

Then adjust  the operating  frequency for  lowest SWR  and record  the frequency.  Now you  can

calculate the capacitance using the formula:

25530

C =

F × F × L

Where C is  the capacitance in picofarads,  F is the frequency in  MHz and L is  the inductance in

microhenries.

4.6 Inductor Measurement

There  are  several  ways  to   measure  inductance  with  the  MR300.  The  simplest  way  is   to

connect  the inductor  across  the  RF  output connector  and  select  Inductance from  the  Mode

pushbutton menu. You  can accurately measure inductor values  as long as the  reactance at the

measurement  frequency is  within  the impedance  measurement  specifications of  the  analyzer

(about 10 to 2000 Ω).

Another  way  to measure  inductance  with  the  MR300  is to  measure  it  in  a  series  resonant

circuit. (See  Figure  1 and  Figure 5).  You  will need  an capacitor  of  known value  and a  51  Ω

carbon composition  or film  resistor. The capacitor  should have a  tolerance no  wider than 10%

and have a low loss dielectric composition such as NP0 ceramic  or mica. A capacitance value of

about 100 pf is appropriate for many RF measurements.

You can make your own  precision capacitor from a piece of coaxial cable. Common  RG-58 type

50 ohm coax has a capacitance of about 29 to 30 pf. For example RG58/U is specified at 28.8 pf

per foot  so a  length of about  3.5 ft  – including  a 1” pigtail  for attachment  will serve as  a fairly

accurate 100 pf capacitor.

December 8, 2016

- 11-

MR300 SWR Analyzer

To measure inductance by the second method, connect the components as shown in as Figure

6.  Adjust the  operating  frequency for  lowest  SWR and  record  the  frequency. Now  you can

calculate the capacitance using the formula:

25530

L =

F × F × C

Where L is  the inductance in microhenries,  F is the frequency  in MHz and C is  the capacitance

in picofarads.

4.7 Measure Inductor Q

The Q of an RF  inductor can be measured with a very simple setup. First measure  the inductive

reactance XL  of the  inductor and  record this  value. Now  connect it  to the  Analyzer as  shown

below in Figure 2.

Figure 2

Capacitor C must be chosen to  resonate with L at the frequency where you want to measure the

inductor’s Q.  The Inductor  and Capacitor Measurement  section of this  manual shows  how this

capacitor value  can be  determined. Now tune  the Analyzer for  the lowest  R (resistance)  value

with a  reading of zero  X (reactance). If  R is above  10 ohms  you can now  calculate inductor Q

using the formula:

XL

R

Q =

If R is less than 10 Ω a slightly different method needs to be used. In this case use the test setup

shown  in Figure  1.  Adding the  noninductive  (carbon composition  or  film)  ¼ or  ½  watt 51  Ω

resistor allows more accurate measurement of the series resistance of the inductor.

Again tune  the  analyzer for  lowest R  (resistance) value  with a  reading of  zero X  (reactance).

Record this  resistance value.  Now connect the  51 Ω  resistor directly across  the analyzer’s  RF

output connector  and measure  its exact  value at  the resonance frequency  and record  it. Next

subtract the exact 51 Ω resistor value from the measured R value and use this new resistance in

the above formula to calculate the Q value.

December 8, 2016

- 12-

MR300 SWR Analyzer

4.8 Transmission line characteristic impedance

The characteristic impedance  of coaxial, twisted pair, open  wire or ribbon type feedlines  can be

estimated using  the MR300. Practical  measurements are  best done in  the mid-tuning range  of

the  instrument   where  accuracy  is   optimum  and  feedline   lengths  are  reasonable;   so  this

procedure will be performed between 7 and 21 MHz.

The  measurements  need  to  be  done  with  a  transmission  line  over  frequencies  where  the

feedline is at  about 1/8 wavelength at the  low frequency end and something  over ¼ wavelength

at the high frequency end, so it is recommended that a length of about 4.9m (16 feet) is used.

Connect  the  near end  of  the  feedline  to the  MR300.  Connect  a  1000 Ω  carbon  or  Cermet

potentiometer to the far end with leads no longer than 2.5 cm (one inch) or so. Initially set the pot

to its highest value, see Figure 6.

Ensure that the transmission line is supported for its entire  length in a fairly straight line and kept

several  inches  from  any  conductive  surface  or  material.  This  is  important  to  minimize any

detuning effects. Ideally the line  should be dressed along to top of a wooden  fence or supported

by fiber rope or string.

Now tune the MR300 over the range of 7-to-21 MHz while noting the resistive (R) and reactive

(X)  values.  More  than  likely  they  will  vary widely  over  the  tuning  range.  Now  readjust  the

potentiometer to a  slightly lower value and  do another sweep while observing  the variation of R

and X values. At some potentiometer setting the R value will vary very little over the tuning range

while the X value will remain near zero. This is the estimated characteristic resistance.

4.9 Transmission line losses

Transmission line  loss  for 50-ohm  feedlines can  be  easily measured  using the  analyzer. The

basic  operating principle  is  that loss  in  transmission  lines attenuates  RF  sent through  them.

When the  line is connected  to the analyzer  and the far  end is short  or opencircuited there  is a

theoretically infinite  SWR. If  the feedline had  zero loss  this would be  the case.  However since

any real  line has  some  loss both  the forward  and reflected  power are  attenuated and  a finite

SWR is measured.

For most  good quality new coaxial  feedlines the loss  at HF frequencies  will not exceed several

dB per  30 meters  (hundred feet);  however as  they age  the dielectric  becomes lossy  to it is  a

good  idea to  periodically  check the  loss.  Measurement is  simple.  All you  have  to do  it  is to

remove the  load, short-circuit the far  end of the  feedline, and then connect  the near end  to the

analyzer’s RF output connector.  Measure the SWR and refer  to table below for the approximate

corresponding loss. If the measured  SWR is above 9:1 that’s good  news since the SWR then is

less  than  1  dB.  If you  vary  the  analyzer  frequency  you  will  see  that SWR   decreases  with

frequency indicating that loss increases at higher frequencies.

December 8, 2016

- 13-

MR300 SWR Analyzer

Approx Loss

1 dB

Measured SWR

9:1

2 dB

4.5:1

3:1

3 dB

4 dB

2.3:1

2:1

5 dB

6 dB

1.7:1

1.6:1

1.5:1

1.4:1

1.3:1

7 dB

8 dB

9 dB

10 dB

4.10 Transmission line stub lengths

Measurement of  quarter and half wave  transmission line stubs  can be performed regardless  of

the  transmission line  characteristic  impedance.  The method  relies  on the  fact  that  an open-

circuited quarter  wavelength line  or a short-circuited  line acts  like a  precise short circuit  at the

chosen frequency of operation.

With  either  type of  feedline  first cut  it  about  10% longer  than  the desired  length,  taking the

appropriate  velocity factor  into  account. The  velocity  factor of  common  feedlines is  available

from manufacturer’s literature or references  such as the ARRL Antenna Book. If you  cannot find

the  value or  if  you  are  using a  custom  type  of  feedline,  the “Velocity  Factor  Measurement”

section in  this manual  provides a  way to  determine this  value. The  following formulas  can be

used to estimate the length of transmission line required.

For a half-wavelength stub the length is:

L = 150000×VF

F

Where L is the length in cm, VF is the velocity factor and F is the operating frequency in MHz for

the stub.

Similarly for a quarter-wave stub use the formula:

L = 7500×VF

F

December 8, 2016

- 14-

MR300 SWR Analyzer

To  determine the  length  of a  half  wave  stub, connect  the  near end  of  the  transmission line

through a 51 Ω resistor as shown in Figure 4  to the analyzer’s RF output connector.  Short circuit

the two leads at the far end of the half wave stub.

Ensure that the transmission line is supported for its entire  length in a fairly straight line and kept

several  inches  from  any  conductive  surface  or  material.  This  is  important  to  minimize any

detuning effects. Ideally the line  should be dressed along to top of a wooden  fence or supported

by fiber rope or string.

Now tune  the MR300  for minimum  SWR  and note the  frequency. This  is the  frequencywhere

the transmission line is exactly  a half wavelength long. If the initial  length was chosen properly it

should be below the desired frequency. If so, cut off a short length making sure the far end is still

short-circuited, and repeat until resonance is achieved at the desired frequency.

For a quarter  wave stub, the  above procedure can be  used except, of course  that the length  is

different and that the far end needs to be opencircuited.

4.11 Transmission line velocity factor

Velocity factor of a transmission line can be measured using techniques similar to the ones used

for measuring  quarter and half  wave stubs. The  procedure can be performed  at any frequency

that the  MR300 tunes  but it  is most  practical in  the vicinity  of 10  MHz where  line lengths  are

reasonable and instrument accuracy is optimum.

Either a  quarter wave or half  wave length can  be used; but  using the shorter  length consumes

less feedline if it will be  discarded after the measurement. Begin by cutting a quarter  wavelength

of feedline using the formula:

L = 7500×VF

F

For a frequency of 10 MHz and assuming a VF (Velocity Factor) of 1.

Now connect  the near end  of the  feedline to a  51 Ω  resistor as shown  in Figure 7  then to  the

analyzer’s  RF   output   connector.  The   far  end   must   be  open   circuited.  Ensure   that  the

transmission line is supported  for its entire length in a fairly  straight line and kept several inches

from  any conductive  surface  or material.  This  is  important to  minimize  any detuning  effects.

Ideally the line  should be dressed along  to top of a wooden  fence or supported by  fiber rope or

string.

Now  tune  the MR300  for  lowest  SWR  and  note  the  frequency.  VF  can now  be  calculated

using the formula:

VF =  10

F

Where F is the measured frequency in MHz.

December 8, 2016

- 15-

MR300 SWR Analyzer

Figure 3,Adjust antenna tuners

Figure 4, ,Adjust antenna tuners

Figure 5, Capacitor or inductor measurement

Figure 6, Determining feedline characteristic impedance

Figure 7, Determining feedline velocity factor

December 8, 2016

- 16-

MR300 SWR Analyzer

5  Command software on PC

The  MR300  is  controllable  from  the  PC  and  allows  the  collection  of  measurements  to  be

processed by  an analysis program.  In the project website  you can find  a simple command  line

program,  PCC-SARK100,  which   performs  control  and  data   capture  from  the  MR300   and

generates a data file compatible with Excel  macro ZPlots from Dan Maguire AC6LA. This macro

performs the analysis of the measures and displays them in different graphs.

URL:  http://www.lxqqfy.com/index/files.php?id=MR100_cmd

The PCC-SARK100  is a simple  command line program  which scans  in the selected  frequency

range and stores the measurement results in a file format supported by ZPlots.

Usage:

PCC-SARK100 -c<com port> -s<start freq> -e<end freq> -t<step value> -o<output file>

Where:

•

•

•

•

•

-c<com port name>

-s<start freq>

-e<end freq>

-t<step>

COM port name

Start frequency in Hertz

End frequency in Hertz

Step value in Hertz

-o<output file>

Output file name (without path)

Example:

》   PCC-SARK100 -cCOM5 -s14000000 -e16000000 -t10000 -oDipole20m.csv

ZPlots

ZPlots is  an Excel macro  developed by Dan Maguire  AC6LA, which provides  the data analysis

and  display graphs  of  the  impedance  data  captured by  the  MR300  antenna. Usage  is  very

simple,   you   select   the   file   captured   by   PCC-SARK100   and   automatically   displays    a

representation  of the  actions  of the  antenna  to the  SWR,  resistance,  reactance, etc..  It  also

represents Smith chart format. In the following pages there are examples of ZPlots graphs.

The complete manual of the original program is available on the project website.

December 8, 2016

- 17-

MR300 SWR Analyzer

6  Windows software on PC

MR300 can also be connected with the Windows application, download from lxqqfy.com.

URL:  http://www.lxqqfy.com/index/files.php?id=MR300_win

December 8, 2016

- 18-

MR300 SWR Analyzer

7  App software on Android

MR300 also connected via Bluetooth and mobile phone, download from lxqqfy.com.

URL:  http://www.lxqqfy.com/index/files.php?id=MR300_app

Bluetooth connection password: 1234

December 8, 2016

- 19-

MR300 SWR Analyzer

8  Battery installation

Because  of  the  transportation   condition  is  not  allowed,  MR300  only   provides  the  battery

interface, does not take the battery.

Battery Specification: 9.6V nickel hydrogen battery, AAA 800mah.

Note: positive and negative pole connection.

Step 1: Open shell.

Step 2: A total of 4 screws.

December 8, 2016

- 20-

MR300 SWR Analyzer

Step 3: Choosing the right battery.

Step 4: Pay attention to the positive and negative.

December 8, 2016

- 21-

MR300 SWR Analyzer

Step 5: Fixed battery.

Step 6: Install back.

December 8, 2016

- 22-

MR300 SWR Analyzer

Appendix A:       USB Driver Installation

The MR300  incorporates a USB  interface for  PC connection. This  interface is  implemented by

the FTDI Chip FT232R  chip which requires prior installation of  a driver "Virtual COM Port (VCP)

available at the following link:

http://www.ftdichip.com/Drivers/VCP.htm

This driver  is available for  multiple operating systems  on which  you access the  manufacturer's

website and  select the appropriate  driver, always  bearing in mind  that the chip  is the FT232R.

Preferably  you   install  by   using  the   "setup   executable"  and   following  the   manufacturer's

instructions.

Once installed  and connected  the MR300  you can  verify proper  installation by  entering in  the

Device Manager  of  the Windows  Control Panel.  By  connecting the  MR300 you  should see  a

new COM  port  with the  FTDI  driver reference.  Please note  the COM  port  name as  it will  be

necessary to  know to  use the MR300  from your  PC, eg for  software updates  or to control  the

instrument from HyperTerminal.

December 8, 2016

- 23-

MR300 SWR Analyzer

Appendix B:      Calibrating the Analyzer

To improve  the accuracy  of the analyzer  this should  be calibrated. This  is a  simple procedure

that just requires loads of  known value and follows the outlined procedures. The  calibration data

is  stored  in   nonvolatile  memory  and  will  remain   stored  during  the  life  of   the  instrument.

Recalibration will be  necessary in the case  of a software  update because the  stored calibration

data are lost during the loading process.

The  instrument normalizes  the gains  of  the four  legs  of the  bridge  for the  different bands  of

operation, creating  the correction  values to  be stored in  nonvolatile memory.  These correction

values  are  calculated   for  different  load  conditions   during  the  calibration  process   and  are

subsequently used for measures to compensate for gain differences of the legs of the bridge.

CalibrationProcedure

1.   Select the "Calibrate" on the setup menu

2.   The  instrument will  prompt the  user with the  LCD text  “Disconnect Load”, indicating  to

remove any  load from the  RF connector. Press  the button VAL  after disconnecting the

load  and  then  the  display  will  show “In  Progress…”  indication  that  calibration  is  in

progress

3.   Then  it will prompt  to connect a  50 Ω load  “Conn 50 Ω Load”.  Plug the 50  Ω load and

then press  VAL.  The display  will show  “In Progress…”  indication  that calibration  is in

progress

4.   After that  it will prompt to connect a 150 Ω load “Conn 150 Ω Load”. Plug the 150 Ω  load

and then press VAL. The display will show “In Progress…” indication that calibration is in

progress

5.   Subsequently it  will prompt to connect a 274 Ω load “Conn 274 Ω Load”. Plug the 274  Ω

load  and   then  press   VAL.  The   display  will  show   “In  Progress…”   indication  that

calibration is in progress

6.   Once   the  calibration  is  finished  it  will  show   the  text  “Done”.  This  means  that  the

calibration process has  been completed and stored  in the EEPROM. Just press  VAL to

continue

December 8, 2016

- 24-

MR300 SWR Analyzer

Appendix C:       Making a Dummy Antenna for Testing

It  may be  desirable  to have  a  dummy antenna  for  testing the  MR300.  A dummy  antenna  is

simply  a  three-component  circuit that  is  resonant  at  a  specific  frequency  and has  a  purely

resistive characteristic at the resonance frequency. The dummy  antenna can be used in place of

a real antenna during initial testing of the instrument.

The dummy  antenna consists  of one  resistor, one  inductor and  a capacitor  in a  series circuit,

built at  the end of  a connector that  can be connected  to the MR300  antenna. The table  below

shows the component values for dummy antennas to any of the specified frequencies:

Freq (Mhz)

7.1

10.1

14.1

18.1

C (pF)

82

47

27

22

L (uH)

6.8

5.28

4.7

3.51

2.08

2.08

Core

T50‐2

T50‐2

T50‐2

T37‐2

T37‐2

T37‐2

#Turns

37

33

31

30

21.2

28.5

27

15

23

23

47Ω

C

L

SingleResonance

December 8, 2016

- 25-

MR300 SWR Analyzer

Appendix D:

PC Command Interface

Command

Description

On

Enables  DDS   signal  generation.   Requires  setting   correct  DDS

frequency

Arguments

Response

‐‐

OK

Error response

Example

Error: freq not set

>>on

OK

Command

off

Description

Arguments

Response

Disables DDS signal generation

‐‐

OK

Error response

Example

‐‐

>>off

OK

Command

freq

Description

Arguments

Response

Sets DDS frequency

{frequency} Frequency in Hertz

OK

Error response

Example

Error: invalid freq

>>freq 14070000

OK

December 8, 2016

- 26-

MR300 SWR Analyzer

Command

imp

Description

Arguments

Response

Get impedance values

‐‐

{SWR},{R},{X},{Z}

Error response

Example

‐‐

>>imp

1.05,52,10,51

Command

raw

Description

Arguments

Response

Get raw bridge voltages

‐‐

{Vf},{Vr},{Vz},{Va}

Error response

Example

‐‐

>>raw

257300,165500,31800,214500

December 8, 2016

- 27-

MR300 SWR Analyzer

Command

Description

scan

Scans  from specified  start to  end  frequency and  get impedance

values

Arguments

Response

{freq_start} Start freq. in Hz

{freq_end} End freq. in Hz

{step} Step in Hz

Start

{SWR},{R},{X},{Z}

{SWR},{R},{X},{Z}

…

End

Error response

Example

Error: expected freq val

Error: expected step val

>>scan

Start

1.05,52,10,51

1.05,52,10,51

..

End

December 8, 2016

- 28-

MR300 SWR Analyzer

Command

Description

Scanr

Scans from  specified  start to  end frequency  and  get raw  bridge

voltages

Arguments

Response

{freq_start} Start freq. in Hz

{freq_end} End freq. in Hz

{step} Step in Hz

Start

{Vf},{Vr},{Vz},{Va}

{Vf},{Vr},{Vz},{Va}

…

End

Error response

Example

Error: expected freq val

Error: expected step val

>>scan

Start

257300,165500,31800,214500

257300,165500,31800,214500

…

End

December 8, 2016

- 29-

MR300 SWR Analyzer

Appendix E:

Quick Reference Sheet

December 8, 2016

- 30-

MR300 SWR Analyzer