Multifunctional LCD Music Spectrum Large Font Clock DIY Kit

Please carefully read the entire production process and then do it will be better!

First talk about the need to pay attention to the problem before soldering.

1. Soldering temperature below 320 ℃, the soldering iron temperature can not be too high.

2. Recommended soldering iron to be grounded and the best is to wear electrostatic bracelet grounding to solder, soldering speed as quickly as possible, or easy to damage the LED dot matrix screen.

3. Make use of high-quality solder with better liquidity.

- Soldering the single chip, the dot on the IC corresponds to the white dot

- Solder chip resistors, chip capacitors and transistors

R1-R2:1M(105)   R3-R6:10K(103)  R7:4.7K(472)  C2,C4:100nF(104)  Q1:9012(2T1)

- soldering LED, LED negative corresponds to letter L1

- soldering DS3231

- soldering  C1（220uF），C3（10uF），U3（AMS1117）

- soldering vibration motor

- soldering switch and photoresistor

Cut off excess pins

- soldering mini USB

- soldering battery holder and buzzer, please pay attention to the welding direction

- All components are soldered as follows

- Solder the pin header to the LCD screen

- Solder the bottom plate to the LCD screen

- Install CR2032 button battery

- Install the acrylic panel, the long plastic pillars are installed on the front panel, as shown below

15．Put on the circuit board

16. Put on short plastic posts

17. Install the rear panel

18. Mounting nut

19. Plug in mini usb cable and one minute two audio cable for power supply

Functions:

Long press the setting key (circular symbol) to switch between four modes: Large Font Time Display Mode---Multiple Information Display Modes---Music Spectrum Effect 1---Music Spectrum Effect 2;

[Only in "Time Display" mode]:

1: Press the setting (circle symbol) + switch touch key (triangle symbol) at the same time to enter or exit the menu;

2: Short touch toggle key (triangle symbol) to switch:

Time Setting---Date Setting---Alarm Clock Setting---Information Template Selection---Format Setting---Birthday Reminder Setting----Brightness Setting---Countdown---Hourly Reminder Setting. Short press the setting key (circle symbol) to enter the setting, and then use the switch key (triangle symbol) to modify the parameter value.

Parameter settings:

1. Time (Set Time): Toggle key (triangle) to modify the flashing parameter value, and set key (circle) to confirm the modification;

2. Date (Set Date): The modification sequence is: year-month-day;

3. Alarm (Set Alarm): ON-turn on the alarm and enter the alarm time setting; OFF-turn off the alarm

4. Display interface (Information Arrangement): TYPE: 1-5 (5 different information display arrangement interfaces); Auto- (automatically switch the display interface mode every day);

5. Display format setting (Set Format): switch button (triangle) to switch three format settings [Time Format (Time Format)-Date Format (Date Format)-Temperature Format (Temp Format)].

Time Format (Time Format): 24-Hour (24 hour mode); 12-Hour (12 hour mode).

Date Format: Month / Date: month-day mode; Date / Month: day-month mode.

Temp Format: Centigrade / .C-degree Celsius; Fahrenheit / .F-degree Fahrenheit;

6. Birthday Remind (Birthday Remind): ON-open reminder function and enter parameter setting; OFF-close reminder

7. Backlight brightness setting (Set Brightness): level: 1-16: (1-16 brightness); Auto: automatically adjust the brightness according to the environment;

8. Countdown setting (Set Countdown): Enter the minutes and seconds, press the set button (circular) to start the countdown, LED flashing and buzzer sound / vibration reminder at the end of the countdown, press any button to exit the countdown;

9. Time Reminder (Time Reminder): Toggle key (triangle) to switch the built-in option settings [Remind Range-Remind Interval]

Remind Range: Enter the start time (inclusive) and end time (excluding). [Note] 00-00 (never remind); 00-24 (24-hour reminder).

Remind Interval: Every 15 Minutes (Remind every 15 minutes); Every 30 Minutes (Remind every 30 minutes); Every Hour (Remind every hour); Every 2 Hours (Every two Hourly reminder).

Note: Toggle the switch to switch between "vibration" and "buzzer" modes.

wiring:

The dual-head audio cable is connected to the music playback device (3.5mm audio hole), one end is connected to the audio plug of the speaker or headphones, and the other end is connected to the audio plug of the "three-head cable" and connected to the 5V USB voltage.

# Text boxes

Put 1 short plastic posts

Put 2 short plastic posts