Sea land air plus（GPS ） Age:14+ Instructions

Please read this manual carefully before installing and using the machine. (the product color and specific

configuration are subject to the real object, and the pictures are for teaching reference only)

Please refer to the operation learning of the video. Remember the basic operation, And then actually operate the flight. Novices need to practice flying on the ground before going to the water. Statement: 1.This remote control model airplane is not a toy. It is suitable for experienced operators. Novice players must carefully remember the correct operation in the manual or video tutorial before practicing flying. You must ensure safe operation, and it is your responsibility to ensure that no harm is caused to others' personal and property. 2. For commissioning and installation, please operate strictly in the installation and operation instructions, and make sure that the head fingers and other parts of the body are far away from the position of propeller and motor, so as to avoid accidental scratches! 3. It is strictly prohibited to fly in roads, railways, airports, high-voltage lines and densely populated residential areas. 4. Please do not fly in bad weather such as strong wind or thunder. 5. Applicable age: must be over 14 years old to use. Don't put it where children can easily reach it! 6. The site area shall not be less than: 200 x 200 (m) (water, land, lawn, etc.) 7. The manufacturer and the Distributor shall not be responsible for any loss or injury caused by the improper use or operation of the user!

I：Basic product parameters

| Fuselage 92 cm Wingspan 66 cm Height from the ground 25 cm Maximum takeoff weight 750g 2.4G six channel remote control 1 Flight control 1 Waterproof steering gear 3 ectric regulation 1 | 2450kv motor 1 Model 6040 propeller 1 Charger 1 11.1v lithium battery 1 Remote control strap 1 Measuring apparatus 1 Fiber tape 1 GPS （Sold separately） |
| --- | --- |
| II：Aircraft power battery installation 1.First, install 4 batteries and 5 batteries on the remote controller, turn on the remote controller switch, and ensure that the throttle is in the minimum state; 2.Then connect the battery with the plug of the electric regulator and install it in the fuselage. Then close the lid and lock the button. (new lithium battery needs to be charged before use) 3.The charging time is about 45 minutes. When the red light and green light are on at the same time, the red light will be full until the green light is on. Note for battery use: 1.Lithium battery should not be over discharged. Once the voltage reaches 11V, it must be charged. If the voltage is lower than 10.5V, it is over discharged, which will cause the battery to be scrapped and can not continue to work. 2.If the battery is not used for a long time, it needs to be kept around 11.4V |
| III：Take off technique 1: Please make sure that the throttle of the remote control is at the minimum position when starting up, and then connect it to the aircraft. GPS needs to be located outdoors.The fifth channel of the remote control switches the GPS function. Up is the GPS mode, down is the balance mode. The positioning time is about 3 minutes, and the ailerons will be fixed. After positioning, the flight mode should be switched to balance mode. （Do not move the aircraft while the GPS is powered, so as not to trigger the automatic return and cause the propeller to start.） 2: Before each take-off, please carefully finish the pre take-off inspection, and check that all equipment of the aircraft can work normally before flying. 3: Slowly push the accelerator to the maximum. After the aircraft starts at a very fast speed, gently pull the tilt rod. The plane flew into the sky. 4: After liftoff, the throttle can be adjusted a little bit. When you want to turn the corner, turn the direction bar straight to one side and let go. The plane will stay level automatically. 5: When the plane is facing you, the direction of operation is the opposite. (the simple way is to turn your head in the direction of the aircraft to adjust the flight direction.) 6: When landing, turn off the accelerator about 20 meters in advance, slowly control the direction of the aircraft to make it land safely, and pull a little head when it is 30 or 40 cm away from the ground or water surface to ensure the safe landing of the aircraft. 7: Shutdown sequence: 1. Unplug the lithium battery first; 2. Turn off the remote control. 8: Note that the lithium battery voltage is lower than 11V must be charged, do not continue to use. In order to avoid the consequences of lithium battery being discarded and unable to be used due to over discharge! 9. Please make sure that the aircraft battery and remote control battery are fully charged. It is recommended to take off against the wind and land against the wind. And fly in the open and flat land. Do not fly in strong wind or bad weather! 11. Please wash the aircraft with fresh water in time after contacting the sea water, so as to avoid the electronic components being corroded and damaged by the sea water. IV：Simple troubleshooting 1. The power of the plane is very weak, and the lithium batteries on the plane need to be recharged. If the voltage of any lithium battery is zero, the battery is scrapped. 2. After starting up, the motor continues to ring, so it is necessary to readjust the trip of the throttle: Throttle travel: when the remote control and the aircraft are off: the remote control throttle to the maximum -- turn on the remote control switch -- plug in the aircraft battery-- two beeps -- quickly pull the throttle on the remote control to the lowest point -- beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep beep. 3. The motor does not turn, usually the electrical regulation is bad or the motor is broken. (this also happens when electricity is diverted into water.) 4. The indicator light of the remote control flashes to alarm, which means the battery of the remote control is dead and the battery of the remote control needs to be replaced. |