Note: The meter head has been calibrated. If there is no 12V power supply, do not enter the 5 mode !! Quickly cut through.

Entering 5 mode will refresh and reset, it needs 12V power to calibrate.

1、Product parameters；

- Voltage measurement range; DC8V-100V

- Working electric current; ﹤ 15MA

- Display mode; LCD screen

-.Display color; blue and white

2. The main feature

- Measurement accuracy: 1% ± 1 digit。

- Display: LCD screen

- Measurement speed: about 2 times per second。

-Dimensions: 61 * 33 * 14.5

3. Product Directions

- The ternary lithium battery L measurement ranges from L02 to 25. Power off memory.

- Lead acid battery P measurement can be from DC12V to 24V, 36V, 48V, 60V, 72V, 84V. Power off memory.

- The lithium iron battery pack F can measure F03 string to 26 string. Power off memory.

4. Product parameter settings, long press the up button to enter the mode selection

-Mode battery type setting：（If the battery does not know the number of strings, you can use the 3 mode, set the high and low voltage）

Power on the LCD display to work, you can now set the type of battery you need to measure. Press and hold the button in the upper right corner of the screen to display 1－－,

Press the up button to switch modes  2－－，3－－，4－－。

Press the down button to display 1－－L，

At this time, press the up button to select L, P, F, etc.。

Press the down button again, the display appears 1－ －L02。

At this time, you can press the up button to set the parameter to be measured, press once to increase the value 。

The ternary lithium battery pack L can be increased by one string at a time。

Lithium iron battery pack F, press one string at a time to measure F03 string to 26 string。

Lead-acid battery: P, increase by 12V at a time, the measurement can be from DC12V to 24V, 36V, 48V, 60V, 72V, 84V.

After setting the battery parameters, press the down button to confirm and save (the value will flash if not saved). The display shows 1--, and the set number of strings (after saving, the value on the display will not flash), then long press the button in the upper right corner to return.

The display shows the parameters of the value you set. Display voltage, power, battery compartment.

Note: If the battery type of mode 1 is not set, only the voltage of the meter will change during battery use, and the power will always be full!

- Mode timing time setting: 2-- display, then press the lower right corner button to display ON 00, OF / ON flashes. After setting the timer time, press the upper button to confirm and save.

Set the start switch OF / ON on the left, and set the timing time on the right (10 seconds, 30 seconds, 60 seconds, 120 seconds)

In this mode, the down key function is to the left →, the up key function is to increase +

- Mode high and low voltage setting 3——  ， 00.0 000 is displayed, (the second decimal point is not displayed, but it exists)

The left is the lowest voltage (the voltage and the following power are displayed with 0% space), the right is the highest voltage (the voltage and the above power are displayed at 100%)

For example: 10.5 135 means the lowest voltage is 10.5V and the highest voltage is 135V.

In this mode, the down key is to the left →, the up key is to increase +

- Mode low pressure alarm function setting  4— —, press the down button to confirm entry， Display 00.0V, OFF

The right alarm start switch OF / ON, and the left is the alarm voltage (alarm when the voltage is lower than this value).

In this mode, the function of the lower key is to the left →, the function of the upper key is to increase +

- Mode calibration voltage setting  5— — ， Display = 12V, (the number will flash) with 12V power supply，

Click the up button, then the right side will be displayed ﹣﹣﹣（Three horizontal bars), OU will be displayed after about 1 second. At this time, it means that the calibration is completed. Press and hold the up button to confirm and save, and return to the main page, which is more accurate。

- Mode temperature display setting  6— —, 。Press the up button to switch the ON / OFF temperature display. The temperature display can be turned off. Press and hold the up button again to confirm the return.

After setting, press the upper key to switch the voltage and temperature display.

- Mode high voltage alarm setting  7— —，Press the down button to confirm entry，Display 00.0V, OFF, at this time the alarm meets and the battery grid will display the battery grid will display full grid, (representing high voltage settings)

In this mode, the down key function is to the left →, the up key function is to increase +

5. Extreme working conditions：

- Operating temperature：-10～+70℃

- Working humidity：10～80%（No condensation）

- Working pressure：80～106kPa

- Sun exposure: no direct exposure

- Do not exceed the specified value of this product during the measurement process, so as not to damage the product

Note: This product is a patented product of our company, please do not imitate, and our company can customize according to customer requirements。