LED音乐频谱电平显示制作套件HU-008

LED Music Spectrum Level Display Making Kit

关于售后服务：

1.可通过微信扫一扫，查看详细说明书（带图片说明）

Detailed installation tutorial can be obtained by scanning QR code on mobile Phone.

Ⅰ.设置说明 Setting Instructions

“RESET”=复位键（背面）；“FUNC”=功能键（侧面）。

亮度调节：在正常状态下，短按“FUNC”键，可改变屏幕的亮度等级。

工作模式设置：长按“FUNC”键(约2~3秒钟），可切换设置内容。短按“FUNC”键可调节选项。设定完成，无操作3~5秒钟后自动退出设置。Under normal conditions, short press the "FUNC" key to change the brightness level of the screen.Working mode setting: long press the "FUNC" key (about 2~3 seconds) to switch the setting content. Short press "FUNC" key to adjust options. After the setting is completed, it will automatically exit the setting after 3 to 5 seconds of no operation.

| 菜单语言设置 Menu language setting | ①按住“FUNC”键始终不放，直到设置结束； Hold down the "FUNC" key until the setting is over; | ②按一下“RESET”键，即进入测试模式 Press the "RESET" button to enter the test mode | ③等待测试进行中出现“ENG”松开“FUNC”键设置为英文；出现“PyC”松开“FUNC”键设置为俄文；出现“中”松开“FUNC”键设置为中文。 Wait for “ENG” and release the “FUNC” key when the test is in progress, and set to English; “PyC” = set to Russian; “中” = set to Chinese . |
| --- | --- | --- | --- |
| 工作模式Working mode | 中文屏幕显示 Chinese screen display | 英文屏幕显示 English screen display | 可选项 /Optional | 功能设置说明 Function setting description | 出厂值 Factory value |
| 频谱显示方式 Spectrum display mode | 方式 N | MODE N | 1 | 普通显示方式/Normal | 2： 浮标 方式 Buoy mode |
|  |  |  | 2 | 浮标显示方式/Buoy |  |
|  |  |  | 3 | 音符显示方式/Note |  |
|  |  |  | 4 | 块状显示方式/Block |  |
|  |  |  | 5 | 柱状显示方式/Columnar |  |
| 声道选择 Channel select | 声 左 右 双 | CHL L R DUAL | 左/Left | 左声道音频输入/Left channel input | 左/Left |
|  |  |  | 右/Right | 右声道音频输入/Right channel input |  |
|  |  |  | 双/Double | 双声道/Binaural（DUAL） |  |
| 重要说明：单声道输入时，需调整此项，以便显示屏能检测到信号显示频谱。 Important Note: When mono input, you need to adjust this item, so that the display can detect the signal display spectrum. |
| 设定小时 Set hour | 时 xy | HOUR xy | 00-23 | 短按按键即可改小时的值 Short press the button to change the hour value | 08 |
| 设定分钟 Set minutes | 分 xy | MIN xy | 00-59 | 短按按键即可改变分钟的值 Short press the button to change the minute value | 08 |
| 自动增益调节功能 Automatic gain adjustment function | 自动 1(0) | GAIN ON(OFF) | 1：开/ON | 开启/Open | 开/Open |
|  |  |  | 0：关/OFF | 关闭/Shut down |  |
| 灵敏度 设置 Sensitivity Set up | 灵度 H（L） | SENS H(L) | H | 对音频反应的灵敏度高 /High sensitivity to audio response | H |
|  |  |  | L | 对音频反应的灵敏度低 /Low sensitivity to audio response |  |
| 时间显示开关 Time display switch | 时显 1(0) | TIME ON(OFF) | 1：开/ON | 打开时钟显示功能 /Turn on the clock display function | 1：开/ON |
|  |  |  | 0：关/OFF | 关闭时钟显示功能 /Turn off the clock display function |  |
| 显示刷新速度 Display refresh rate | 显 速 1-8 | SPEED 1-8 | 1-8 | 显示刷新速度从慢到快 /Display refresh rate from slow to fast | 6 |
| 频谱显示顺序 Spectrum display order | 音 序 顺序 (优化) | DISP SEQ | 顺序/order | 频谱显示由低到高顺序排列/Spectrum display arranged from low to high | 顺序排列/Order |
|  |  |  | 优化/optimization | 频谱显示按优化的顺序排列/Spectrum display arranged in optimized order |  |
| 其它设置 Other settings | 其 他 N(1-8) | OTHER N(1-8) | 1-8 | 设置自动增益状态下的频谱显示的平衡度。/Set the balance of the spectrum display in the automatic gain state. | 3 |
| 1.在三极管其中一个焊盘先上焊锡。Solder solder on one of the pads of the transistor first. | 2.夹持元件焊接，补齐剩余引脚。Welding of clamping components to fill the remaining pins. | 3.以同样的方法焊接101贴片电阻。 Solder 101 chip resistors in the same way. | 4.焊接贴片晶振、30PF贴片电容。（无极性） Solder SMD crystal, 30PF SMD capacitor. (No polarity) | 5.焊接153贴片电阻、106贴片电容。 Solder 153)chip resistor and 106 chip capacitor. | 6.焊接104电容，100、334、474贴片电阻。 Solder 104 capacitors, 100, 334, 474 chip resistors. |
| 7.剪短电解电容的引脚，对应丝印图案焊接。（白条为-） Cut the pins of the E-cap, corresponding to the soldering of the silk screen pattern. (White bars are -) | 8.以同样的方法焊接2脚贴片按键。 In the same way, solder the 2-pin SMD button. | 9.同样的方法焊接4脚贴片侧按键。 Use the same method to solder the 4-pin SMD side button. | 10.同样的方法焊接3.5mm音频接口。 Weld the 3.5mm audio interface in the same way. | 11.最后焊接MINI USB接口，如上图所示。 Finally,welding MINI USB interface, as shown above. | 1.撕去外壳保护膜后，先将螺丝穿过正面外壳，如上图所示。 After removing the protective film of the case, first pass the screw through the front case, as shown in the figure above. |
| 2.如上图所示将电路板穿过螺丝，并用铜柱固定。 Pass the circuit board through the screws as shown in the figure above and fix it with copper posts. | 3.对应安装四周边框，如上图所示。 Corresponding to the border around the installation, as shown above. | 4.用螺丝（长）和螺母固定支脚，注意【RESET】按键的位置。 Fix the feet with screws (long) and nuts, pay attention to the position of the [RESET] button. | 5.在背面外壳对应位置贴上圆形硅胶垫，用于触发【RESET】按键。Attach a round silicone pad to the corresponding position on the back shell to trigger the [RESET] button. | 6.最后盖上背面外壳，并用螺丝（短）固定，如上图所示。 Finally, close the back cover and fix it with screws (short), as shown in the figure above. |  |

# Text boxes

Ⅱ.焊接步骤及外壳组装Welding & Shell installation