蓝牙音箱制作套件 HU-009

Bluetooth Speaker Making Kit

关于售后服务：

1.售后时间：上午10点—12点，下午13点—18点（周一到周六）

2.可通过微信扫一扫，查看图文说明书（带图片说明）

Detailed installation tutorial can be obtained by scanning QR code on mobile Phone.

Ⅰ.元件清单BOM

Ⅱ.电路原理&元件分布图  Schematic&Component map

| 1.焊接直插电阻12K、330Ω、10K、33K。Welding DIP resistor 12K, 330Ω, 10K, 33K. | 2.焊接M18蓝牙音频模块。Welding M18 Bluetooth Audio Module. | 3.焊接HT6872音频功放芯片。 Weld the HT6872 audio power amplifier chip. | 4.焊接拨盘电位器50K（503）。 Welding dial potentiometer 50K (503). | 5.焊接104独石电容。 Weld 104 monolithic capacitors. | 6.焊接3.5mm音频插座。 Solder 3.5mm audio socket. |
| --- | --- | --- | --- | --- | --- |
| 7.焊接KA2284电平驱动芯片。 Weld KA2284 level driver chip. | 8.焊接卧式侧按键。 Welded horizontal side buttons. | 9.焊接直插电解电容（引脚长正短负）。 Solder in-line electrolytic capacitors (pin length is positive and short is negative). | 10.焊接蓝白电位器10K(103)。 Solder the blue and white potentiometer 10K (103). | 11.如下图按顺序焊接5mm LED。 Solder 5mm LEDs in sequence as shown below. | 12.焊接卧式自锁开关。 Welding horizontal self-locking switch. |
| 13.最后焊接喇叭线、USB电源线。 Finally,Weld the speaker wire and USB power cord. | 1.铜柱、M3螺母固定电路板，并用M3螺丝锁在底面外壳。 Copper pillars and nuts are used to fix the circuit board, and use screws to lock the bottom shell. | 2.用M3螺丝、螺母将喇叭固定在正面外壳。 Use M3 screws and nuts to fix the speaker on the front shell. | 3.对应安装侧面外壳，并用M2螺丝、螺母固定。Install the side shell correspondingly and fix it with M2 screws and nuts. | 4.安装顶面及背面外壳，注意USB电源线从底面外壳卡槽引出。Install the top and back shells, and pay attention that the USB power cord is led out from the bottom shell slot. | 焊接组装完成展示图 |

# Text boxes

详细焊接&外壳组装步骤请扫描二维码查看图文教程。For detailed welding & shell assembly steps, please scan the QR code to view the graphic tutorials.