TEA5767数字广播套件

TEA5767Digital broadcast Kit

关于售后服务：

1.产品核对：开箱验货，确定无误再签收，如有问题请及时联系客服

2.售后时间：上午10点—12点，下午13点—18点（周一到周六）

3.可通过手机扫码，查看图文说明书（带图片说明）

Ⅰ.元件分布图 Component distribution diagram

Ⅱ.电路原理图 Schematic

Ⅳ.焊接步骤及注意事项 Welding steps and precautions

焊接详细步骤请扫描二维码获取Please scan QR code for detailed welding steps.

# Text boxes

↑本套件电路板有设置一处故障点，请扫描上方二维码查看具体详情。

↑There is a fault point on the PCB of this kit. Please scan the QR code above for details.

Ⅲ.元件清单  BOM

| 序号 | 名称 | Name | 标号/Label | 数量/Number |
| --- | --- | --- | --- | --- |
| 1 | 电路板 | PCB | / | 1 |
| 2 | 262小天线 | Antenna-262 | X1 | 1 |
| 3 | 4位数码管 | 4-digit nixie tube | / | 1 |
| 4 | 100UF 50V电解电容 | E-CAP 100UF 50V | C3,C9,C11 | 3 |
| 5 | 10UF 25V电解电容 | E-CAP 10UF 25V | C7,C8 | 1 |
| 6 | 22PF 瓷片电容 | Ceramic-CAP 22PF | C1,C2 | 3 |
| 7 | 104独石电容 | MONO CAP 104 | C4,C5,C6 | 4 |
| 8 | 自锁开关 | Self-locking switch | S4 | 1 |
| 9 | 自锁开关帽 | Switch cap | / | 1 |
| 10 | DC005电源座 | Power socket-DC005 | 5V | 1 |
| 11 | 4.7欧电阻 | Resistor-4.7Ω | 4.7 | 1 |
| 12 | 10K电阻 | Resistor-10K | 10K | 11 |
| 13 | 220K电阻 | Resistor-220K | R3 | 1 |
| 14 | S9012三极管 | Triode-S9012 | Q1,Q2,Q3,Q4 | 5 |
| 15 | 13.56M晶振 | Crystal-13.56M | Y1 | 1 |
| 16 | TEA5767收音机模块 | FM-Tuner TEA5767 | TEA5767 | 1 |
| 17 | 按键 | Button | / | 2 |
| 18 | LED 白发兰发光二极管 | LED-white to blue | D13 | 1 |
| 19 | 50K拨盘电位器 | Dial potentiometer-50K | R6 | 1 |
| 20 | 8P IC座 | IC socket-8P | LM386 | 1 |
| 21 | 40P IC座 | IC socket-40P | U1 | 1 |
| 22 | LM386芯片 | Chip-LM386 | LM386 | 1 |
| 23 | STC89C52(烧写好程序) | Chip-STC89C52 | U1 | 1 |
| 24 | 5V2A电源适配器 | Power adapter-5V2A | / | 1 |
| 25 | 喇叭 | Speaker | / | 1 |
| 26 | 外壳包 | Shell pack | / | 1 |
| 27 | 双通铜柱 | Double Copper Post | / | 若干 |
| 28 | M3*8mm螺丝 | M3*8MM screws | / | 若干 |
| 29 | M3*12mm 螺丝 | M3*12MM screws | / | 若干 |
| 30 | M3螺母 | M3 Nuts | / | 若干 |

1.焊接贴片收音模块时，先焊接一个引脚固定，确认模块放置准确后再焊接剩余引脚。

First weld one pin for fixation, and then weld the remaining pins after confirming that the module is placed accurately.

2.根据丝印标识焊接4.7Ω、220K、10K电阻（11个）。（特别注意R3电阻为220K）

Weld 4.7 Ω, 220K and 10K(11) resistance according to the silk screen mark. (note that R3 resistance is 220K)

3.根据丝印标识焊接晶振(Y1)、22P瓷片电容（C1/C2）、104独石电容（C4/C5/C6）。

Welding crystal oscillator (Y1), 22P ceramic chip CAP (C1/C2), 104 MONO CAP

(C4/C5/C6)shall be identified according to the silk screen.s

4.根据丝印标识焊接拨位电位器，如图示。

Weld the shift potentiometer according to the silk screen mark, as shown in the figure.

5.焊接C7电解电容时，需放倒焊接。（短引脚为负极，对应丝印图案白色阴影）

When welding C7 electrolytic capacitor, it is necessary to place it upside down for welding. (short pin is negative, corresponding to white shadow of silk screen pattern)

6.根据丝印标识焊接4.7Ω、220K、10K电阻（11个）。（特别注意R3电阻为220K）

Weld 4.7 Ω, 220K and 10K(11) resistance according to the silk screen mark. (note that R3 resistance is 220K)

7.根据丝印图形标识焊接S9012三极管、4位数码管。

Weld s9012 triode and 4-digit nixie tube according to the silk screen graphic identification.

8.根据丝印标识焊接LED（长引脚为正极，短引脚为负极）、DC005电源座。

Weld the LED,Power socket-DC005 according to the silk screen mark. (LED:long pin is positive, short pin is negative)

9.根据丝印标识焊接100uF、10uF电解电容，如下图所示。

Weld 100uF and 10uF E-CAP according to the silk screen mark, as shown in the figure below.

10.根据丝印标识焊接自锁开关、按键、天线，如下图所示。

Weld the self-locking switch, button and antenna according to the silk screen mark, as shown in the figure below.

11.焊接喇叭接线，红+黑-，如下图所示。等组装好喇叭外壳后再将导线焊接至电路板对应的接口。

Welding horn wiring, red + Black -， as shown in the figure below. After assembling the horn shell, weld the wire to the corresponding interface of the PCB.

焊接完成示意图Welding completion diagram