Step 1: Soldering the wire to the + and - poles of the LED strip, and weld the current limiting resistor to the negative pole or series in the middle of the black line.

第一步：把电线焊接在灯条正负极上，把限流电阻焊在负极或者串联在黑色线中间。

Step 2: Wrap the LED strip around the transparent plastic.Secure with sellotape.

第二步：把LED灯带缠绕一圈在透明塑料件上。可以用透明胶带固定四个角。

Step 3: loosen the screws on the left and right .

第三步：把左右侧的旋钮开关螺丝松掉。

Step 4: Place the luminescent component inside the remote control panel.

第四步：把发光组件放入遥控面板内部。

Step 5: Place the aluminum cover on top of the plastic light emitting module.

第五步：把铝合金面盖放在塑料发光组件上面。

Step 6: Re-install the joystick assembly and secure it with the provided longer screws.

第六步：把摇杆组件重新安装回去，用所配的加长螺丝固定好。

Step 7: Use a multimeter to measure the positive and negative poles of the 5V step-down module

第七步：用万用表测量找到5V降压模块的正负极。

Step 8: Welding the positive and negative electrodes of the LED strip to the 5V step-down module. Pay attention to the positive and negative electrodes.

第八步：把LED灯条的正负极焊接在5V的降压模块上，注意正负极。

You're done!

第九步，合上面盖，通电，大功告成。Dung!

# Text boxes

ZOOM IN