Multifunctional vacuum cleaner manual

- Introduction of main parts:

- Brush tightness switch

- Long suction nozzle

- Dust collecting cover

- Power indicator

- Vacuum switch button

- Type-C charging port

- Rear air outlet

- Cover

II. Precautions before operation:

* Before the use , confirm whether the parts are assemble correctly , especially pay attention to the filter assembly in the dust box.

* Please fully charge the machine for the first time or if it has been stored for a long time. The charging indicator red light will turn off when it is fully charged

* Note that it can be turned on during charging it. But try to avoid use them when charging.

* This product is not waterproof, please do not suck a lot of water or liquid to avoid the damage, especially flammable and explosive substances such as chemical solvents or alcohol.

* Do not inhale highly hot substances (such as burning cigarette butts or hot ash) to avoid burning the filter or plastic parts to make them lose the function.

* If there is the loudly abnormal sound during the use, you should stop using it immediately to check if the filter is lost ! If the installation is finished , please contact the after-sales department to confirm the treatment.

* Please put it in a cool place without using it . Do not place it in a position  more than 60 ℃  to avoid fire hazard.

III. Instructions for use:

Vacuum function:

* Remove the cover first

* Long press the vacuum switch to turn on.

It is equipped with long suction nozzle and brush, which can be used flexibly. Press the button again to turn off.

IV. Product charging:

* When the product has been used for a long time and the suction of the vacuum motor is obviously decelerated, the product needs to be charged before it continues to be used.

* Use the standard Type-C interface plug. It is recommended to use a charger with output voltage of 5.1V and current above 2A to charge the product.

* Connect the type-C charging cable to charging port(⑥). The red light(④) is always on when it is charging, will turn off after it is fully charged.（The machine that has just been finished working needs to be shut down for about 10 minutes and let the temperature of the machine fall down before it can be charged)

* This product is specially designed for type-C port. Therefore, additional charging cable is attached for customers' conveniently use!

V. Faults and troubleshooting:

| Cause of issue | Possible Causes | Countermeasures |
| --- | --- | --- |
| Can not work/No power | * Battery is too low * Press the wrong buttons | * Charge in time *Press the right button |
| Unable to vacuum | * The dust box is not installed * The filter is blocked | * Check for corrections * Instant cleanup |
| Abnormal noise | * Foreign matter is blocked at the suction nozzle * The filter is missing | * Check and clean it * Install filter |

VI. technical parameter:

| Product name | Multifunctional vacuum cleaner |
| --- | --- |
| Product mode | V9 |
| Battery capacity | 2200mAH |
| Rated power | 70W |
| Rated voltage | 7.4V |
| Charging parameters | 5V 1.8A |
| Charging port | Type-C |
| Net weight | 630g |
| Product size | Φ71*303mm |