Frequency and power control method

●Support BF firmware OSD to adjust frequency and power, among which PIT mode is 0mw, which is used for short-distance tuning.

●Key control: frequency adjustment: short press--times to change the number of channels CH (CH1-CH8); frequency group selection: long press the button for 2 seconds

(FR blue light flashes) Enter the frequency group switching mode, then short press the button to change the frequency group FR (A-F); power adjustment button power

Control: Long press the button for 10 seconds (the LED light is displayed as shown in the figure below) to enter the power switching mode, and then short press the button to change

Power rating 25mw/100mw/200mw;

|  | 25mw | 100mw | 200mw | Fault |
| --- | --- | --- | --- | --- |
| Frequency group indicator FR | ○○● | ○●○ | ●○○ |  |
| Channel number indicator CH | ○○● | ○●○ | ●○○ |  |
| Power indicator | Flash 1 stop 3s | Flash 2 and stop 3s | Flash 3, stop 3s | Always bright① |

Note①: The power indicator in PIT mode is also always on, here it means that it is not in PIT mode.

Frequency table

Pandarc Frequency Tab1e (Mhz)

| Pandarc Frequency Tab1e (Mhz) |
| --- |
| CH FR | CH1 ○○○ | CH2 ○○● | CH3 ○●○ | CH4 ○●● | CH5 ●○○ | CH6 ●○● | CH7 ●●○ | CH8 ●●● |
| A | ○○● | 5865 | 5845 | 5825 | 5805 | 5785 | 5765 | 5745 | 5725 |
| b | ○●○ | 5733 | 5752 | 5771 | 5790 | 5809 | 5828 | 5847 | 5866 |
| C | ○●● | 5705 | 5685 | 5665 | 5645 | 5885 | 5905 | 5925 | 5945 |
| d | ●○○ | 5740 | 5760 | 5780 | 5800 | 5820 | 5840 | 5860 | 5880 |
| E | ●○● | 5658 | 5695 | 5732 | 5769 | 5806 | 5843 | 5880 | 5917 |
| F | ●●○ | 5362 | 5399 | 5436 | 5473 | 5510 | 5547 | 5584 | 5621 |
| Blue light indicates FR, green light indicates CH, hollow circle means off, solid circle means bright. |