OPERATI NG MANUAL

November 2016

# when you get a new VAC9010H voltage ammeter, it is recommended that you follow the following steps to check the instrument.

- Check for damage caused by transportation.

If serious breakage of packing carton or bubble bag protection pad is found, please keep it first until the whole machine and accessories pass the test.

- check if the items in the packing box are complete.

The contents of the packing box are described below. If the content does not match or the instrument is damaged, please contact the dealer or our company.

Host :1 VAC9010H( including display head and power expansion board)

Annex :1 user manual (version pdf)

3. check the whole machine.

If you find that the appearance of the instrument is damaged, the instrument is not working properly, or fail to pass the performance test, please contact the dealer or our company.

# Chapter I Overview

## I. Introduction to Instruments

VAC9010H voltage ammeter is a new type of voltage ammeter which can measure voltage, current, charge and discharge capacity, time, power and so on. At the same time, it can set parameters to realize overvoltage protection, undervoltage protection, overcurrent protection, overcharge capacity protection and time limit protection.The instrument uses non-contact Hall sensor to detect the current safely and conveniently, and the instrument uses color liquid crystal to display the measured data, the display information is comprehensive and humanized. This instrument is very suitable for the need to monitor the output voltage and current, as well as for battery charging and discharge applications.

## Main characteristics

1. bidirectional detection of current, for the detection of charge and discharge users can automatically identify and detect bidirectional current,

no need to change wiring direction.

2. power off memory function, after power off can remember the number of AH before power off, easy to observe and measure.

3.AH number and current zero clearing function, does not affect the next measurement.

4. voltage, current, charge capacity AH number, WH number, time, power display at the same time, the display information is comprehensive and clear.

5. with output off function key, flexible turn on or off output (need to be relayed).

6. has over-voltage, over-current, over-power, time limit, over-charge and other protection functions.

7. can be calibrated online to facilitate customers to correct errors in time.

8. display LCD screen can be extinguished manually or automatically after less than 300 mA a minute.

9. through the Hall sensor to detect the current, the current through the wire can pass through the sensor round hole, positive and negative direction current can be detected, safe and convenient.

The last page summarizes the operational techniques

## III. TECHNICAL INDICATORS

| Type | VAC9005H | VAC9010H | VAC9020H | VAC9030H |
| --- | --- | --- | --- | --- |
| Current measurement range | 0-50 A | 0-100 A | A 0-200 | A 0-300 |
| Display resolution | A 0.01 | 0.1 A | 0.1 A | 0.1 A |
| Voltage measurement range | Self-powered (12-90) V external powered (0-90) V more than 90 V need to contact customization |
| Current accuracy | ±3±5 words |
| Voltage accuracy | ±2%±5 words |
| Display resolution | Voltage | V 0.01 |
|  | Capacity | AH 0.01 |
|  | Time | 0.01H（1min） |
| Measurement rate | 5 times per second |
| Protection Type and Setting | OVP (overvoltage protection) | 0.01 V~90 V |
|  | OPP( Overpower Protection) | 0.01 W~9.99 KW |
|  | LO P (undervoltage protection) | 0.01 V~90 V |
|  | OCP (overcurrent protection) | 0.1~100 A |
|  | OAH (overcharge protection) | AH 0.01 AH~999 |
|  | OFT (Timeout Protection) | min ~99 hour59min 1 |
| Size (length × width × height) | 79×43×52(mm) |
| mounting hole opening (mm) | 76.5*39.2(mm) |

Table 1-1 VAC9010H Technical indicators

# Chapter II Instrument Description

## I. Panel description

## The instrument is a split structure, which consists of two parts: instrument and power expansion board. figure 1-1 is the instrument front panel, figure 2-1 is the instrument front panel description.

## Figure 1-1 VAC9010H Front panel

| Label | Note |
| --- | --- |
| 1 | Voltage values |
| 2 | Current value |
| 3 | Capacity percentages and progress bars |
| 4 | AH number (blue), power value (yellow) |
| 5 | WH number (blue), time value (yellow) |
| 6 | Protection Select menu |
| 7 | Press button |

Figure 2-1 VAC9010H Front panel description

## II. Wiring description

## This diagram shows the circuit in discharge mode, charging only need to change the load into a charger, no need to change the circuit. The current direction enters from the front of the transformer and flows out from behind, that is, the residual electricity quantity of the instrument decreases; conversely, the residual electricity quantity increases.

1. Fig .1 is the power supply connection mode of no relay

Figure 1 VAC9010H Description of Power Expansion Board Connection

When in use, first connect the "BAT" terminal to the power supply, then the battery to the positive or nearby line of the load, one of which passes through the round hole of the Hall transformer, then check whether the jumper cap is at the J4, and finally plug the terminal of the terminal line connected to the positive and negative electrode of the battery into the" BAT" place "on the expansion board.Be careful to follow the schematic wiring, can not reverse, wrong connection.

2. Figure 2 shows the power supply connection mode of independent power supply without relay

Figure 2 VAC9010H Description of Power Expansion Board Connection

When using, first connect the power supply at the "BAT" terminal, then connect the battery to the positive or nearby line of the load, one of which passes through the round hole of the Hall transformer, then check whether the jumper cap is at the J3, it is best to plug the terminal of the terminal line connected to the positive and negative electrode of the battery into the expansion board" BAT", the independent power supply (12 v-60v) is connected, and the power can be powered on.Be careful to follow the schematic wiring, can not reverse, wrong connection.

3. Figure 3 shows the power supply connection mode of independent power supply with relay

Fig .3 VAC9010H Power Expansion Board Interface Description

When using, first connect the "BAT" terminal to the power supply, then connect the battery to the positive or nearby line of the load, one of which passes through the round hole of the Hall transformer, then check whether the jumper cap is at the J3 and then connect the relay. Finally, plug the terminal of the terminal line connected to the positive and negative electrode of the battery into the" BAT"" on the expansion board.Be careful to follow the schematic wiring, can not reverse, wrong connection.

Description: Relays need to be equipped by the user, standard with no relay.

# Chapter III Use Notes

## I. Wiring

Select the appropriate wiring mode according to the range of the voltage measured to ensure that the input voltage is within the range of the meter.

Note: Input voltage range :10 V ~90 V; when self-powered

input voltage range when external power supply :0 V ~90 V, greater than 90 V consult remarks when need purchase.

## Output

if the relay is connected, move the yellow cursor to the OUT by clicking the button    after electrification, click the OK key to control the output, if the OUT light is shown as green, the output is turned on, if the OUT light is gray, the output is turned off, and the machine power-on state defaults to the state before the last shutdown.If the relay is not used, the output is always on and the OUT lamp fails.

## III. Expanding Function Setup

If you want to turn on an extension, move the yellow cursor to the corresponding item, click the OK button to turn the indicator light of the corresponding item into green, turn on the protection and turn it into gray. Before opening the protection to set the protection parameters, the method is long press OK key about three seconds into the protection function parameter settings page, and then by adjusting the key to increase or reduce the set parameters. After setting the parameters, click the OK key to return to the initial interface, the default parameters of each function when leaving the factory are all 000.

Note: If the parameters are not adjusted after entering the adjustment page, you need to press it once, and click the OK key to return to the initial page.

## IV. Introduction of Extended Function

1." OVP" overvoltage protection, if the OVP value is set, and the OVP protection option is turned on, when the input voltage exceeds the set voltage, the machine will automatically cut off the output, at this time the OUT lamp changes from green to gray. To restore the output after the protection is turned off, move the yellow cursor to "OUT", click OK key from the newly opened output.

2." OPP "is over power protection, if OPP value is set, and the OPP protection option is turned on, when the output power exceeds the set power, this machine will automatically cut off the output, at this time the OUT lamp changes from green to gray. To restore the output after the protection is turned off, move the yellow cursor to "OUT", click OK key from the newly opened output.

3." OCP "is overcurrent protection, if the OCP value is set, and the OCP protection option is turned on, when the input current exceeds the set current, the machine will automatically cut off the output, at this time the OUT lamp changes from green to gray. If you want to restore the output after the protection is turned off, turn off the protection option first and restore the normal output.

4." OFT "is timeout protection, if the OFT value is set, and the OFT protection option is turned on, when the working time exceeds the set time, the machine will automatically cut off the output, at this time the OUT lamp changes from green to gray. To restore the output after the protection is turned off, move the yellow cursor to "OUT", click OK key from the newly opened output.

5." OAH "is super capacity protection, if the OAH value is set and the OAH protection option is turned on, when the accumulated AH value exceeds the set value, the machine will automatically cut off the output, at this time the OUT light changes from green to gray. If you want to restore the output after the protection is turned off, turn off the protection option first and restore the normal output. The percentage of capacity display is the actual measured value compared to the set number of AH: capacity percentage =(actual AH / set number)*100%.

6." lOP "is undervoltage protection, if the lOP value is set, and the lOP protection option is turned on, when the actual voltage value is lower than the set protection voltage, this machine will automatically cut off the output, at this time the OUT lamp changes from green to gray. To restore the output after the protection is turned off, move the yellow cursor to "OUT", click OK key from the newly opened output.

7. can turn off the screen manually (yellow cursor moves to the OVP, long press the button to turn off the screen) current less than a certain value can automatically turn off the screen, press the OK key to open the screen.

- AH number and time clearing function. Move the yellow cursor down to "LOP", and then click on the key , when the yellow cursor disappears, then click on the OK key, the time zero, you can clear the number of AH zero or full, AH number plus full value corresponding to" OAH" set value.

The current A number zero clearing function, when the no-load current value is not 0, the yellow cursor can be moved to "OUT", long press the OK key for 3 seconds, zero until zero.

9." OUT" arrow function. when the arrow behind the OUT "is green and points to the left, the current is the inflow state AH the number will increase over time. when the arrow behind the OUT" is red and points to the right, the current is the outflow state AH the number will decrease over time. pay attention to the wiring mode when wiring.

# Attention and maintenance

1. can not exceed the meter voltage and current range use, otherwise will damage the meter.

2. the positive and negative poles can not be connected back, the connection back can not be measured correctly.

3. operating temperature-10~50℃, storage temperature-20 and 70℃, and keep the instrument in a dry environment.

4. do not try to disassemble this instrument, breaking the package will cause warranty failure. There are no parts within the instrument that users can repair. The repair can only be done through the designated repair outlets or sent back to our factory.

Do not move the instrument violently 5. the instrument is working properly so as not to cause irreparable damage to the internal circuit.

# Warranty and after-sales service

thank you for purchasing the products of sine electronics studio. To maximize the functionality of your new product, we recommend the following simple steps:

1. read safe and effective use guidelines.

2. read warranty terms and conditions.

Warranty conditions:

The warranty period is one year from the date of delivery of the instrument. During the warranty period, the company chooses to repair or replace the faulty instruments according to the circumstances. For maintenance, please mail this product to our company.

The following are not covered by warranty:

Improper operation or maintenance by the user; use the software or interface provided by the user himself; modify the instrument without permission.

VAC9010H bi-directional voltage ammeter operation notice

1. The screen can be turned off manually, but the screen needs to be turned on manually; it can also have a current value of less than 300 mA lasting one minute automatically, and the current is higher than 300 mA automatically lit;

Operation: The yellow cursor moves to the OVP place, continues to press the key, the screen extinguishes, recovers presses the OK..

2.OAH power settings (recommended to be charged can release the value of electricity), yellow cursor moved to the OAH, long press the OK key into the parameter settings, after the completion of the key to save the settings; it is recommended that the first full charge of electricity once.

Operation: The yellow cursor moves to the position of the LOP, press the next key again, the yellow cursor disappears, then press the OK key, the power is full / zero cycle.

3.The full voltage measured is set in the OVP, e.g. the full voltage 48 V,OVP parameter can set 47.8 V、47.9V, slightly lower than the full voltage, and the charge voltage reaches this value. OVP inside voltage parameter, below 10 V is 0.01 V change, above 10 is 0.1 change.

4.No load current correction, yellow cursor moved to the OUT, long press the OK key 3 seconds to let go, can be repeated operation, zero until.

5, the supply voltage up to 12 V, head can be stable and normal operation, the voltage is too small, easy to cause a weak runout.

# Text boxes

VAC9010H

Bidirectional Voltage Ammeter

Voltage Meter